Documentation for monster.dot and related files
The graphic in monster.dot describes the Wishbone master and slave connections defined in monster.vhd and related vhd files.
## monster.dot
The nodes of the graph are the interfaces described by the SDB. The edges of the graph are the connections
- Wishbone master → Wishbone slave [black]
- Crossbar → Wishbone slave [black]
- Wishbone master → Crossbar [black]
- crossbar → crossbar [red]
- MSI master → MSI slave [blue]
Some components defined in VHDL have a couple of interfaces. These components are depicted with a blue frame and the name of the component.
The label of each node starts with the number displayed by eb-ls on a timing receiver with one LM32 core (e.g. exploder5, pexarria5). For SCUs (two LM32 cores) and data masters (four LM32 cores) these numbers are shifted.
	1 LM32	2 LM32	4 LM32
WB4-MSI-Bridge-GSI	8	8, 9	8, 9, 10, 11
LM32-RAM-User	12.4.5	13.14.[5,6]	15.14.[5,6,7,8]

## monster.ods
This spreadsheet lists identifiers and types from VHDL, SDB product names. Parent crossbars, and other infos for the interfaces.
“eb-ls output” shows the output from eb-ls on a timing receiver with one LM32 core.
“monster.vhd” is collected from monster.vhd, ftm_pkg.vhd, wr_core.vhd, and further VHDL files. Show for each component and its interfaces:
1. the parent component
2. the instance id in monster.vhd
3. the name of the constant for this instance as defined in monster.vhd
4. the category of this component
5. the name of the SDB constant as defined in monster.vhd
6. the HDL data type
7. the product name from SDB
8. the device id from SDB
9. the vendor id from SDB
## monster.pdf
This file is created from monster.dot with
dot -Tpdf monster.dot -o monster.pdf
# Generating monster.dot automatically from monster.vhd and related VHD files
Sketch of the actions to build monster.dot:

Categries of nodes (components in FPGA):
1. Crossbar, including optional MSI part
2. Wishbone Master
3. Wishbone Slave
4. Wishbone Bridge (Master + Slave between two crossbars)

Categories of edges (component is connected to another component on FPGA)
1. From crossbar to crossbar
2. From crossbar to Wishbone slave
3. From Wishbone master to crossbar
4. From Wishbone slave to MSI part of crossbar

Steps to get nodes and edges:
1. Step: Get all SDBs from HDL files. This simplifies search for product definitions, since all
definitions are in one text file.
Use in dev/master/bel_projects:
grep --directories=recurse --include=*.vhd -A5 -B10 -iE 'Vendor_id[ ]*=>' > Monster-VendorIDs.txt
grep all SDB definitions (10 lines before, 5 lines after 'Vendor_id') from all HDL files into
the file Monster-VendorIDs.txt

2. Step: Collect input for Monster.ods
In monster.vhd locate a crossbar definition. For all constants (are unique) in this definition,
locate the constant (not unique, some products are used multiple times) for the SDB definition.
Search for the SDB defintion of this product (use Monster-VendorIDs.txt for this or the HDL files in
folder 'modules'. Use the HDL type, product name (not unique), device id, and vendor id from this
definition. The category of the component is defined in the crossbar definition. The parent component
is the name of the crossbar. The instance id is in monster.vhd.

3. Step: Coding of monster.dot
Step through all crossbar definitions and instance definitions in monster.vhd.